## Slide 1: IMUL
signed multiplication

## Slide 2
There are two main forms of the IMUL instruction:
IMUL operand
IMUL operand1, operand2

## Slide 3
One-Operand Form:
IMUL Operand
This is similar to MUL. This form multiplies the register RAX by the operand, and the result is stored in the RDX:RAX pair. The most significant 64 bits of the result are stored in RDX, and the least significant 64 bits are stored in RAX.

## Slide 4
Two-Operand Form:
IMUL operand1, operand2
This form multiplies the second operand by the first operand and stores the result in the first operand register. In this case, RDX is not inherently used unless it is explicitly specified as the destination operand.

## Slide 5
When dealing with the IMUL instruction (signed multiplication):
whether or not the RDX register is used to store part of the result depends on the specific form of the IMUL instruction being used.

## Slide 6
In the two-operand form, what happens if the result of the IMUL is too large to store in the first operand?

## Slide 7
In the two-operand form:
if the result of the multiplication is too large to fit in the 64-bit destination register, the overflow will not be stored in another register; instead, the result will be truncated to fit within the 64-bit destination register. This means that only the least significant 64 bits of the result are kept, and the most significant bits (which cannot fit) are discarded.

## Slide 8
Unlike the one-operand form of IMUL:
which stores the overflow into the RDX register, the two-operand form does not inherently provide any direct indication of overflow within the registers. To detect an overflow condition from a two-operand IMUL, you would need to analyze the flags in the RFLAGS register

## Slide 9
The Carry flag (CF) and the Overflow flag (OF) are set:
if the result is too large to be represented in the destination register, indicating an overflow condition. These flags need to be checked after the operation if the preservation of the full result or the detection of an overflow is important to the logic of the program

## Slide 10
In summary:
For IMUL in 64-bit mode, RDX is used to store the most significant 64 bits of the result only in the one-operand form of the instruction, where the operation affects the RDX:RAX register pair. In the two-operand form, RDX is not used to store the result unless it is explicitly specified as the destination operand and we need to check the OF and CF to know whether an overflow has occurred.